## Slide 1: DICOM deid

## Slide 2: Image deid
Filter corrupt files (super big or small file sizes)
Use machine learning to filter to stuff we wanted (i.e. B-Mode, M-Mode, views, etc.)
Run images through EasyOCR, perform regex on the strings, categorize:
  low risk (known safe whitelist)
  medium risk (only a few characters, stuff that showed up consistently)
  high risk (strings long enough to be PHI, stuff that looked like dates or times)
Spot check the medium risk images, manually review all high risk images
Remove PHI (entire record, or black out problematic pixels)

## Slide 3: Metadata deid
Characterize the DICOM tags in the data
  tag, tag_name, value_rep, data_type, n_total, n_unique, min_len, max_len, min_value, max_value
Use pydicom to perform deid
  Create a recipe to set a rule for each DICOM tag
    Custom deid functions can be applied to tags
Type of tag | Deid
Name, address, phone number | REMOVE, or BLANK
Study ID, MRN | CUSTOM - shift
Date, time | CUSTOM – shift per MIMIC
Operator name, station name | CUSTOM – encrypt (FPE)
Instance UIDs | CUSTOM – create lab UID

## Slide 4: Metadata deid
Respect required tags: https://dicom.nema.org/dicom/2013/output/chtml/part05/sect_7.4.html
Respect rules for each tags value representation (VR): https://dicom.nema.org/dicom/2013/output/chtml/part05/sect_6.2.html
UIDs
  * SOP Class UIDs, Transfer Syntax UID, Implementation Class UID are typically not sensitive so don’t need deid
  Instance UIDs (and others) may contain sensitive information such as raw study identifiers
    We created a deid ID specific to our lab:
      1.2.840.113554.6.1.104.112747525839636706729436544020735086604
      MIT_ID.LCP_ID.MIMIC_ID.TAG_ID.SHA512_derived_hash
    Not recommended but alternatively you could also create a generic 2.25 UID by appending a universally unique ID: https://dicom.nema.org/medical/dicom/current/output/chtml/part05/sect_B.2.html
      2.25.UUID_v4
      Must follow UUID v4 rules – certain digits must contain certain values
      Need to register your ID?
Notes: The SHA512 algorithm was fed an entropy string composed of the subjects mrn, a salt specific to the variable name, and the value of the variable itself.
We decided to get our own lab identifier instead of using a 2.25 UID so we wouldn’t be constrained by the UUID restrictions and to provide clear information about where the ID came from and what each digit refers to. To get a institution specific ID check these resources: https://www.iana.org/assignments/enterprise-numbers/ https://www.iana.org/assignments/enterprise-numbers/assignment/apply/

## Slide 5: Metadata deid
pydicom
  recipe
    REPLACE StudyID func:map_study_id REPLACE AcquisitionDateTime func:shift_datetime
    BLANK AccessionNumber
    REMOVE PersonName REMOVE PersonAddress
    ADD PatientIdentityRemoved YES
  custom deid functions
    class DeidDataset:
    def pseudonymize(self)
    parser.define('map_study_id', self.map_study_id)
    parser.define('shift_datetime', self.shift_datetime)
    def map_study_id(self)
  calling the deid deid_pipeline = DeidDataset(recipe, other_paramaters)
    dataset = pydicom.dcmread(dicom_file)
    dicom_scrubbed = deid_pipeline.pseudonymize(dataset)